## Slide 1: Start of Row implementation
Pernav
Edward
22nd of October 2026

## Slide 2: intro
Gave the start of row algorithm a go
Developed in python
  Not yet a ROS2 node
AI developed but step-by-step

## Slide 3: Processing steps

## Slide 4: Stitch PCL’s
Single PCL
Septentrio rearAxle
EoR from Joram
Note: pcl colors are due to segmentation explained a few slides into the future

## Slide 5: Stitch PCL’s
2s window
Extrapolate EoR to previously unseen region
  Limited to +10m

## Slide 6: Add LIDAR FoV

## Slide 7: Segment pcl
Uses EoR x and y axes

## Slide 8: RANSAC
One per segmented PCL
  Retain 99% of points

## Slide 9: RANSAC
Common heading fit
  Computes average heading
  Weighted by no. of inliers in each pcl

## Slide 10: SoV
Find start of vines
  Find first point along common heading
  Remove if not in locally dense region
    5 points in 0.25m radius
  Remove if too close to LIDAR FoV boundary

## Slide 11: SoV Line
(Nearly) LS between all SoV
  Exclude 1 outlier IF NOT on headland side
OK like this, or can we think of something better?

## Slide 12: metrics
Heading error
XY error

## Slide 13: parameters
Tried to limit this

## Slide 14: validation
Last Linden fieldtest
Compute time per pcl: [0.01 .. 2.6]s
  Linked to no. of PCL points
  Approx. linear with window

## Slide 15: Next steps
SoV line fitting improvement?
Speed-up:
  Remove unnecessary computations
  Optimize RANSAC parameters
  RoI selection 
  Downsampling based on local density?
Track SoR over time?
Make node
Test on Jetson
???

## Slide 16: Speed-up
Reduce to 1s stitching window
Downsample dense regions for RANSAC (common) heading, use full pcl for SoVs
Remove segmented PCLs that cross the LIDAR FoV
Result
  Seems to be capped at <0.5s
  Good enough for now?

## Slide 17: validation
Updated with speed-up improvements

## Slide 18: Steps
2-step RANSAC
Rear axle validation